CMake
Build system for modern C++
(Dieter Kybelksties)

---
Background
- C++ is a compiled language as opposed to interpreted language (like Python, bash)
- A C++ compiler translates a C++-text into native binary (assembly)
- 3 phases
  - Pre-compile
  - Compile
  - Link

---
C++ code as compact as possible
- Additional information is needed to compile from C++-text to binary
- Additional information can be complex, and there can be a lot of it
  For example command-line to compile 1 file into an object file:

---
When does the pre-compiler need parameters?
The pre-compiler recursively replaces #include instructions with contents of files.
The #include instructions are usually only filenames, sometimes with relative paths. So where do we find these files?
Variable definitions/references in code

---
When does the compiler need parameters?
Which C++ standard to use (compile against)
Compile for performance or debug
Whether to compile for different architecture (cross-compile)
Whether to treat warnings as errors
Output location for compiled (object) files
…
Command parameters need to be added for every single file that is compiled

---
When does the linker need parameters?
- The input for the linker are the object files created by the compiler, plus (static or dynamic) libraries, so we need locations for all the files
- Symbolic or static linkage
- Location of linker to use
- ...

---
In summary need to instruct our compiler:
- Where to find files/headers/libraries – this can be lots of different folders
- Attributes we want our executable to have
  - Create debuggable binary?
  - High-performant?
  - Create for a different hardware (cross-compile)?
  - Dynamic/static?
  - ...
- Use external tools or pre-compilers (eg. lex/yacc)?
- This information is usually given as parameters to the comile command
  - -I : include path
  - -D: variable definition
  - -o: output-filename
  - -L: library directory
  - -Wall: Turn on all warnings
  - ...

---
Traditionally we used Makefiles
- On Posix systems the standard: Makefiles – normally one for each folder .
  In the makefiles we declared targets and a recipe for how to build each target.
  To make this process a bit more general we could define
  - variables (much like shell-variables)
  - Dependencies
  - General recipes
  This was very cumbersome end error prone.

---
Next iteration: autotools
Microsoft (in VisualStudio) used visual tools to define XML documents to simplify the creation of Makefiles.
Unix/Linux used autotools (automake,...). Autotools would search standard directories to find:
- “Known” directories, and whether and where specific libraries and tools are installed
- whether and where specific headers are installed
- Check capabilities of compiler and linker, like C++-standard etc.
- Autotools worked and made things easier, but remained a dark art for many

---
CMake
For a few years now cmake has been the weapon of choice to define and configure builds of C++ projects.
- Similar in approach to the way autotools works
- Generates Makefiles or Ninja files
- Text-based
- Descriptive
- Well-documented
- Powerful
- Well maintained and community supported

---
Minimal example
File CMakeLists.txt:
- If the C++ file mini.cc exists and is a valid C++-program source, this would be sufficient to build a simple executable with cmake
- The executable would be called my_exe.

---
Exercises
- Create a folder and unzip CMakeExercises.tar.gz into this folder (tar -xvf CmakeExercises.tar.gz)
- Each of the folders Step01 - Step07 contains a file __INSTRUCTIONS__.md – a markdown text-file – that tells you what to do.

---
Do excercises
>>>

---
Variables, functions
set(<variable-name> <variable-value>)
function(<function-name> [parameter] [...])

---
Flow-control
foreach(…) for example create similar targets:
Is equivalent to:

---
Cmake help pages
- String operations: https://cmake.org/cmake/help/latest/command/string.html
- If-then-else: https://cmake.org/cmake/help/latest/command/if.html
- Find libraries: https://cmake.org/cmake/help/latest/command/find_library.html
- Find a program: https://cmake.org/cmake/help/latest/command/find_program.html
- Run bash commands: https://cmake.org/cmake/help/v3.0/command/execute_process.html
  and more